## Slide 1: Ch.3.
Factors Affecting WQ
  Geology
  Climates
  Geography
  Plantation/Biological activities
  Human beings-pollution

## Slide 2
  Geological factors on WQ
    Structure/Texture: Controls
      Residence time of water (reaction time)
      Pathways of water migration
    Types of rocks (=mineral compositions): Controls
      Reaction types
      Kinds of the constituents (WQ criteria) and their concentrations

## Slide 3: Geology really controls WQ?
For Chuncheon stream water (From Yu et al, 1994)

## Slide 4
For the groundwater from Indian Wells-Owens Valley, CA
(from Güler and Thyne 2004).

## Slide 5
    Mineral-Water interactions
      Adsorption/desorption
      Ion exchanges
      Dissolution & precipitation
      (Hydration/htdrolysis)

## Slide 6: Adsorption-Desorption
J
Aqueous or gas phase
Adsorption
Desorption
Adsorbent
Adsorbate

## Slide 7: Adsorption Models
      Empiricial
Distribution, Langmuir, Freundlich, etc.
      Surface complexation
          Constant capacitance
          Diffusive electric double layer
          Triple layer etc.
≡S + J = ≡S-J

## Slide 8: Heavy metal removal from the stream water (Yu and Heo, 2001)
Variations of the dilution factor (D) and removal fractions (Ri) of the dissolved metals along Imgok Creek: a, October 1996; b, April, 1997; c, October, 1997. Data from Yu and Heo (2001).

## Slide 9: Ion Exchange
I+
Aqueous or gas phase
J+
Exchangeable sites
I+
I+
I+
I+
J+
J+
J+
J+
J+
Exchangeable cations

## Slide 10: Equilibrium expressions for ion exchange
      Gains-Thomas convention (Gains and Thomas, 1953)
      Vanselow convention (Vanselow, 1932)
      Gapon convention (Gapon, 1933)
Ii+/i + J-Sj/j = I-Si/i + Jj+/j

## Slide 11: Flushing of salt water below a clay layer
From Appelo & Postma (1993)
Porosity = 0.3
Flushing salts in pore space = 40 yrs
Removal of exchangeable Na+ by Ca2+ = 457 yrs
Removal of exchangeable Mg2+ by Ca2+ = 249 yrs
Total of 746 yrs of cleaning
Dutch Wadden sea Islands

## Slide 12: Dissolution & Precipitation
Dissolution
Precipitation

## Slide 13: Description of dissolution & precipitation
      Equilibrium approach
When τR>>τ1/2, Keq = ∏aiνi
      Kinetic approach
  Otherwise, dCi/dt = νik∏ Cini
aA + bB + cC + ∙∙∙∙ = iI + jJ + kK + ∙∙∙∙

## Slide 14: Mineral stability in the stream water
from Yu et al. (1994)

## Slide 15: Fe contents in stream water controlled by the precipitation schwertmannite and ferrihydrite
from Yu et al. (1999)

## Slide 16: Water hardness in England
www.coastalguide.org/england/engrcol.html
www.brookwater.co.uk/water_softeners.shtml

## Slide 17
      Arsenic in groundwater
        Possibly from anthropogenic and natural sources
        Naturally As concentration is very low (<10ppb)
        Naturally high [As] usually due to redox reactions of As mienrals
        Causes cancer, health effects on various skin and intestinal parts

## Slide 18: Arsenic problems in worldwide
1 US Unknown 8 India 1,000,000
2 Mexico 400,000 9 Bangladesh 50,000,000
3 Chile 437,000 10 Thailand 1,000
4 Bolivia 20,000 11 Vietnam Millions
5 Argentina 2,000,000 12 Taiwan 200,000
6 Hungary 20,000 13 China 720,000
7 Romania 36,000 14 Nepal Unknown
from http://www.mindfully.org/Water/2003/Arsenic-Legacy-Worldwide6aug03.htm

## Slide 19: Arsenic poisoning (arsenosis)
Bangladesh
http://www.siliconeer.com/past_issues/2000/may2000.html

## Slide 20: References
Appelo, C.A.J. and Postma, D. (1993) Geochemistry, Groundwater and Pollution. Balkema, Rotterdam, 536p.
Gains, G.L. and Thomas, H.C. (1953) Adsorption studies on clay minerals. II. A formulation of the thermodynamics ofexchange adsorption. J. Chem. Phys., 21, 714-718.
Gapon, E.N. (1933) Theory of exchange adsoption (in Russian). V. J. Gen. Chem. (USSR), 3, 667-669.
Güler, C and Thyne, G.D. (2004) Hydrologic nd geologic factors controlling surface and groundwater chemistry in Indian Wells-Owens Valley area, southeastern California, USA. J. Hydrol., 285, 177-198.
Langmuir, D. (1997) Aqueous Environmental Geochemistry. Prentice Hall, Upper Saddle River, NJ, 600p.
Vanselow, A.P. (1932) Equilibria of the base-exchange reactions of bentonite, permutites, soil colloids and zeolites. SOil Sci., 33, 95-113.
Yu, J.-Y. and Choi, I.-K. (1994) Adsorption of trace metals on the natural amorphous iron oxyhydroxide from the Taebag coal mine area. J. Kor. Soc. Groundwater Environ., 1, 23-32.
Yu, J.-Y.. Choi, I.-K., and Kim, H.-S. (1994) Geochemical characteristics of the surface water depending on the bed rock types in the Chuncheon area. J. Geol. Soc. Kor., 30, 307-324.
Yu, J.-Y. and Heo, B. (2001) Dilution and removal of dissolved metals from acid mine drainage along Imgok Creek, Korea. Appl. Geochem., 16, 1041-1053.
Yu, J.-Y., Heo, B., Choi, I.-K., Cho, J.-P., and Chang, H.-W. (1999) Apparent solubilities of schwertmannite and ferrihydrite in natural strea waters polluted by mine drainage. Geochim. Cosmochim. Acta, 63, 3407-3416.